## Slide 1
  内核移植实例

## Slide 2
  Linux内核移植
  网卡驱动移植
  SD/eMMC驱动移植
    USB主机控制器驱动移植
内容提要

## Slide 3
嵌入式linux系统移植步骤
  准备开发板和相关资料
    要了解开发板的相关配置（有那些外围设备等）
  下载内核源码、取得相关工具软件
    kernel，toolchain etc.
  选定参考板
    选择一个内核中已经支持，且和自己的开发板相似的参考板为模板，进行修改
Linux内核移植

## Slide 4
  修改开发板相关代码
    完成BSP的修改移植
    如：arch/arm/mach-exynos/
    如果使用设备树则修改设备树文件
    如：arch/arm/boot/dts/exynos4412-origen.dts
  添加驱动
  编译、调试、下载内核
Linux内核移植

## Slide 5
移植相关目录和代码
arch/arm/mach-exynos
arch/arm/plat-samsung
arch/arm/tools/mach-types
arch/arm/Kconfig
arch/arm/Makefile
arch/arm/boot/compressed
arch/arm/boot/dts/
Makefile
Linux内核移植
添加基本驱动
  闪存驱动（MTD NAND）
  串口用来打印信息
    可以在内核启动之前打印信息
    内核启动后可以通过console打印信息
网络支持可以使得开发调试更为方便
  如挂载网络文件系统 nfs

## Slide 6
顶层Makefile
  Makefile
    ARCH=arm
    CROSS_COMPILER=arm-cortex_a8-linux-gnueabi-
    ……
    vmlinux: $(vmlinux-lds) $(vmlinux-init) $(vmlinux-main) vmlinux.o \
    $(kallsyms.o)
    ……
Linux内核移植

## Slide 7
arch/arm/Makefile
  machine-$(CONFIG_ARCH_EXYNOS) := exynos
  ifneq ($(machine-y),)‏
  MACHINE := arch/arm/mach-$(machine-y)/
  else
  MACHINE :=
  endif
  textofs-y := 0x00008000
  TEXT_OFFSET := $(textofs-y)
  ‏
arch/arm/mach-exynos/Makefile.boot
  zreladdr-y := 0x20008000
  params_phys-y := 0x20000100
Linux内核移植

## Slide 8
arch/arm/boot/Makefile
  ZRELADDR := $(zreladdr-y)‏
  PARAMS_PHYS := $(params_phys-y)‏
  INITRD_PHYS := $(initrd_phys-y)
  export ZRELADDR INITRD_PHYS PARAMS_PHYS
Linux内核移植

## Slide 9
基本移植
  拷贝设备树文件
  cp arch/arm/boot/dts/exynos4412-origen.dts arch/arm/boot/dts/exynos4412-fs4412.dts
  在Makefile中添加新的设备树文件的编译项
  $ vim arch/arm/boot/dts/Makefile
  exynos4412-origen.dtb \
  exynos4412-fs4412.dtb \
  修改设备树文件
  删除firmware节点。这是TrustZone相关的程序，并未提供。
  firmware@0203F000 {……};
Linux内核移植

## Slide 10
  生成默认配置
  make ARCH=arm exynos_defconfig
  修改配置
  $ make ARCH=arm menuconfig
  General setup --->
  (arm-none-linux-gnueabi-) Cross-compiler tool prefix
  编译
  $ make ARCH=arm uImage -j2
  $ make ARCH=arm dtbs
  测试
  将uImage和设备树下载到开发板的内存中，使用bootm命令启动内核
Linux内核移植

## Slide 11
网卡移植
  添加设备节点，参考：
  原理图
  Documentation/devicetree/bindings/net/davicom-dm9000.txt
  Documentation/devicetree/bindings/interrupt-controller/interrupts.txt
  Documentation/devicetree/bindings/arm/gic.txt
  reg = <0x5000000 0x2 0x5000004 0x2>;
  interrupt-parent = <&gpx0>;
  interrupts = <6 4>;
网卡驱动移植

## Slide 12
  添加驱动配置
  Device Drivers --->
  [*] Network device support --->
  [*] Ethernet driver support --->
  <*> DM9000 support
  [ ] Force simple NSR based PHY polling (NEW)
  添加网络配置
  [*] Networking support --->
  Networking options --->
  <*> Packet socket
  <*> Unix domain sockets
  <*> PF_KEY sockets
  [*] TCP/IP networking
  [*] IP: kernel level autoconfiguration
网卡驱动移植

## Slide 13
  添加网络文件系统配置
  File systems --->
  [*] Network File Systems --->
  <*> NFS client support
  <*> NFS client support for NFS version 2 (NEW)
  <*> NFS client support for NFS version 3 (NEW)
  [*] Root file system on NFS
  时钟相关代码修改
    参考Documentation/clk.txt：Part 6 - Disabling clock gating of unused clocks，可以通过bootargs进行参数传递，也可以直接修改代码。
    drivers/clk/clk.c：529：static bool clk_ignore_unused = true;
  重新编译并测试
网卡驱动移植

## Slide 14
SD/eMMC驱动移植

## Slide 15
SD卡主机控制器节点
sdhci@12530000 {
bus-width = <4>;
pinctrl-0 = <&sd2_clk &sd2_cmd &sd2_bus4>;
pinctrl-names = "default";
cd-gpios = <&gpx0 7 0>;
cd-inverted = <0>;
status = "okay";
};
SD/eMMC驱动移植

## Slide 16
驱动配置选项
Device Drivers --->
<*> MMC/SD/SDIO card support --->
<*> Secure Digital Host Controller Interface support
<*> SDHCI support on Samsung S3C SoC
SD/eMMC驱动移植

## Slide 17
文件系统选项
File systems --->
DOS/FAT/NT Filesystems --->
<*> MSDOS fs support
<*> VFAT (Windows-95) fs support
(iso8859-1) Default iocharset for FAT
-*- Native language support --->
<*> Codepage 437 (United States, Canada)
<*> Simplified Chinese charset (CP936, GB2312)
<*> ASCII (United States)
<*> NLS ISO 8859-1 (Latin 1; Western European Languages)
<*> NLS UTF-8
SD/eMMC驱动移植

## Slide 18
USB主机控制器驱动移植

## Slide 19
USB主机控制器驱动移植

## Slide 20
usbphy: usbphy@125B0000 {
#address-cells = <1>;
#size-cells = <1>;
compatible = "samsung,exynos4x12-usb2phy";
reg = <0x125B0000 0x100>;
ranges;
clocks = <&clock 2>, <&clock 305>;
clock-names = "xusbxti", "otg";
status = "okay";
usbphy-sys {
reg = <0x10020704 0x8>;
};
};
USB主机控制器驱动移植

## Slide 21
ehci@12580000 {
usbphy = <&usbphy>;
status = "okay";
};
usb3503@08 {
compatible = "smsc,usb3503";
reg = <0x08 0x4>;
connect-gpios = <&gpm3 3 1>;
intn-gpios = <&gpx2 3 1>;
reset-gpios = <&gpm2 4 1>;
initial-mode = <1>;
};
USB主机控制器驱动移植

## Slide 22
Device Drivers --->
[*] USB support --->
<*> EHCI HCD (USB 2.0) support
<*> EHCI support for Samsung S5P/EXYNOS SoC Series
<*> USB Mass Storage support
<*> USB3503 HSIC to USB20 Driver
USB Physical Layer drivers --->
<*> Samsung USB 2.0 PHY controller Driver
SCSI device support --->
<*> SCSI device support
<*> SCSI disk support
USB主机控制器驱动移植